IP11
IP11–03 REVERSE LAMPS RELAY DRIVE: TO ACTIVATE, IC SWITCHES CIRCUIT TO GROUND
IP11–05 ENGINE OIL PRESSURE SIGNAL: ENGINE OIL PRESSURE PRESENT = GROUND
IP11-07 BATTERY POWER SUPPLY: B+
IP11-08 POWER GROUND: GROUND
IP11-11 IGNITION SWITCHED POWER SUPPLY (II): B+
IP11-13 GNITION SWITCHED POWER SUPPLY (I): B+
IP11-15 SIDE LAMPS STATUS: B+ WHEN ACTIVATED
IP11-17 DIP BEAM STATUS: B+ WHEN ACTIVATED
IP11-19 AIR BAG WARNING: HARD WIRED TO AIR BAG INDICATOR
IP11-21 DIMMER CONTROLLED ILLUMINATION: PWM, 80 Hz, GROUND = 0% DUTY CYCLE, B+ = 100% DUTY CYCLE; HARD WIRED TO BACK LIGHTING; MICRO SENSED FOR DISPLAY
IP11-24 POWER STEERING (NOT USED)
IP11-25 ???

IP10
IP10-01 REVERSE LAMP SWITCH: B+ WHEN ACTIVATED
IP10-02 SECURITY INDICATOR DRIVE: TO ACTIVATE, IC SWITCHES CIRCUIT TO B+
IP10-03 PATS 1: ENCODED COMMUNICATION
IP10-04 PATS 2: ENCODED COMMUNICATION
IP10-05 PATS GROUND: GROUND
IP10-06 PATS TRANSCEIVER POWER: B+
IP10-07 FUEL LEVEL SENSOR 1 SIGNAL: VARIABLE RESISTANCE: 20 R = EMPTY; 160 R = FULL
IP10-08 FUEL LEVEL SENSOR 2 SIGNAL: VARIABLE RESISTANCE: 20 R = EMPTY; 160 R = FULL
IP10-09 FUEL LEVEL SENSOR REFERENCE: GROUND
IP10-10 MAIN BEAM STATUS: B+ WHEN ACTIVATED
IP10-11 WASHER FLUID LEVEL LOW SIGNAL: FLUID LEVEL LOW = GROUND
IP10-12 BRAKE FLUID LEVEL WARNING SIGNAL: FLUID LEVEL LOW = GROUND
IP10-13 EMERGENCY UNLOCK: B+ WHEN ACTIVATED
IP10-15 PARKING BRAKE SIGNAL: PARKING BRAKE ON = GROUND
IP10-16 TRIP COMPUTER CYCLE SWITCH: GROUND WHEN ACTIVATED
IP10-17 CAN +
IP10-18 CAN -
IP10-19 FRONT FOG STATUS (HARD WIRED TO INDICATOR): B+ WHEN ACTIVATED
IP10-20 REAR FOG STATUS (HARD WIRED TO INDICATOR): B+ WHEN ACTIVATED
IP10-22 SCP +
IP10-23 SCP -
IP10-24 TRIP COMPUTER MODE SIGNAL: STEPPED RESISTANCE
IP10-25 TRIP COMPUTER SWITCH PACK REFERENCE: GROUND